## Slide 1
Light-Based Secure File Transfer System
Team Members: Samyak Gandhi (22BCP082), Tiyarsna Solanki (22BCP066)
Under Guidance of: Ms. Ashka Raval
Department of Computer Engineering

## Slide 2
The Challenge
Security Risks
Digital data exchange poses threats in sensitive environments
Restricted Access
USB, Wi-Fi, Bluetooth banned in high-security zones
Data Breaches
Espionage and evidence tampering risks

## Slide 3
Our Solution
Covert LED Communication
Offline file transfer using optical channel
No Wi-Fi dependency
No Bluetooth required
No USB connections
Trace-less transmission

## Slide 4
Key Applications
Military Bases
Secure communication in air-gapped defence environments
Forensic Labs
Evidence transfer without contamination or tampering risks
Research Centres
Confidential data exchange in isolated research facilities

## Slide 5
How It Works
Binary Conversion
File converted to binary data
Manchester Encoding
Data encoded for synchronisation
LED Transmission
Light pulses transmit signal
LDR Detection
Receiver captures variations
File Reconstruction
Binary decoded to file

## Slide 6
Why Manchester Encoding?
Simple OOK Pulsing
Sensitive to intensity & noise
Hard to distinguish 0 & 1
Synchronisation issues
Higher bit error probability
Manchester Encoding
Works in noisy environments
Clear 0 & 1 differentiation
Self-synchronising signal
Lower transmission errors

## Slide 7
System Architecture
Transmitter
Arduino Nano + High-brightness LED
Receiver
LDR + Op-Amp + Microcontroller
Error Protection
CRC/checksum verification

## Slide 8
Technical Components
01
LED Control
Digital PWM pin controls LED intensity
02
Light Detection
LDR senses intensity variations
03
Signal Amplification
LM358 Op-Amp converts analogue response
04
Binary Conversion
Microcontroller converts voltage to bits

## Slide 9
Experimental Results
1-2m
Transmission Range
Stable indoor communication distance
Low
Bit Error Rate
Manchester encoding ensures accuracy
Performance Factors
LED brightness levels
Ambient light conditions
Distance between devices
Noise reduction techniques
Watch demonstration: https://docs.google.com/videos/d/18DjlHtdivheL-Mq4qNrJ0a2_oUj4Y41KF22Ju8IuWzc/play

## Slide 10
Future Enhancements
Laser & Photodiode
Higher speed and longer range transmission
AES-128 Encryption
Enhanced security layer for data protection
Bi-directional Communication
Full-duplex data exchange capability
ML Noise Filtering
Machine learning for improved accuracy
Mobile Interface
User-friendly app for easy operation

## Slide 11
Conclusion
Secure & Covert Transfer
Our system offers a low-cost, secure, and untraceable method for file transfer.
Overcomes Restrictions
Effectively operates in high-security zones where traditional networking is prohibited.
Versatile Applications
Proves highly beneficial across forensics, defence, and research facilities.
Viable LED Communication
Successfully demonstrates the effectiveness of LED-based optical communication for data transfer.
Thank You!